## Slide 1
DORY - Mission Overview
TEAM Politecnico DI MILANO
ESA/ESEC (Concurrent Engineering Challenge 2025)

## Slide 2: Mission Overview
GOAL
Mass | 3643.81 kg
Margined ∆V | 2581.32 m/s
Dimensions | 3.82 x 3.05 x 2.92 m
Study comet shape and mass distribution
Map the surface of a comet
Investigate the in-depth composition
To mesure the on-site magnetic disturbances
Return at least 10g of samples on Earth
Target Comet: 304P/ORY

## Slide 3: Architecture selection
Criterion | Monolithic satellite | Satellite + Lander
Mass | 5 | 4
Science Output Depth of sampling | 4 | 5
Science Output Mass of sample | 5 | 4
Cost | 5 | 3
Reliability | 3 | 2
MONOLITHIC SATELLITE
Simpler
Lighter
Touch and Go strategy
Cheaper
Less critical events
SATELLITE + LANDER
More complex
Heavier
Landing strategy
More expensive
Lower TRL for in-situ PL
Trade-Off analysis (5 is best)
MONOLITHIC SATELLITE

## Slide 4: CONOPS

## Slide 5: CONOPS
HP: Hold Point

## Slide 6: Modes
Modes | Definitions
Science - Remote | Mapping of the comet
Science - TAG | Touch and Go
Science – Rad-Mag | Comet study with radar and magnetomer
Maneuver - DSM | Deep space maneuver
Maneuver - OCM | Orbital correction maneuver
Telecom - LP | Low power telemetry communication
Telecom - HP | Science data downlink
Transfer | Interplanetary transfer
Safe | Power saving mode
Detumbling | Reduce s/c angular rate
Approach | Approach to the comet
Desaturation | Desaturation of the reaction wheels
Commissioning | Testing of all the subsystems

## Slide 7: Payload Paolo Fedele Di Giglio Gabriele Farina Matteo Fulgheri Moein Peyghambarzadeh

## Slide 8: Requirements and Assumptions – Payload
REQ ID | STATEMENT
MR-03 | The mission shall return at least 10g of samples to Earth.
MR-04 | The mission shall investigate the elemental composition of a comet to at least a depth of 30cm (requirement), and should investigate a depth of up to 1m (goal).
MR-08 | The mission shall investigate the elemental composition of 100% of the surface of a comet with a resolution of 2m.
SR-05 | The system shall allow for the identification of at least one landing site.
SR-10 | The system shall be able to monitor and provide data of magnetic disturbances in 3 axes.
Input from MA
The semi-major axis during surface mapping is 10 km.

## Slide 9: Analysis and Trade-offs – Payload
Sample Collection
Landing vs Touch&Go approach
Projectile vs Gas
Sample Conservation Analysis
Comet Enviroment Analysis
Depth Investigation
Drill sampling vs Remote observation
SAR vs Radar Sounder
Mass, power and data budgets
Vertical resolution
Time of Observation
Surface Mapping
Camera properties (FOV, spatial resolution)
Mass & Power Budgets
Time of Observation
Altitude analysis
Notes: Most critical requirement -> MR-04
Analyze internal structure of the comet through radar sounder instead of direct sample collection.
Dielectric properties + mass distribution = geological structure.
--> Talk about Time/# acquisition/data volume for radar

## Slide 10: Final Baseline Design – Payload
Instrument | Req ID | Mass + DMM [kg] | Power [W] | Data Rate | Data Volume
Framing Camera (DAWN) | MR-08 SR-05 | 5.775 | 17 | 20.5 Kbps | 10.3 GB
Radar (SHARAD MRO) | MR-04 | 17.955 | 28 | 20 Mbps | 10 GB
Magnetometer (MESSENGER) | SR-10 | 1.50 (boom 2.8) | 4.2 | 0.414 Kbps | 267 MB
Camera resolution: 93.7 µrad
Camera FOV: 5.5 x 5.5 deg
Camera wavelengths: 400-1050 nm
RADAR frequency: 20 Mhz
MAG resolution: 0.047 nT

## Slide 11: Final Baseline Design – Payload
 | Temp. [°C] | Pressure [Pa]
*GCS | <- 80 | <500
**SCS | <- 60 | Vented
*GCS = gas containment system
**SCS = solid containment system
GCS & SCS concept from CAESAR mission
Decoupling volatile/solid
Temperature/pressure conditioning
Sample container stow in SRC
Sample Return Capsule Closure
Notes: Possible to use the same approach of the CAESAR concept Sample Return Capsule, passive cooling system.
Volatile & Solid separation.
Sublimation transfer of volatile components to GCS is made by a complex mechanism of slowly warming up.

## Slide 12: Mission Analysis Davide Bellini Alessandra Centrella Francesco Persenico Davide Provenzi

## Slide 13: Requirements and Assumptions – MA
ASSUMPTIONS
STATEMENT | COMMENTS
No drag is considered during the close proximity Phase | Low activity of the comet when this phase occurs
Impulsive manoeuvres | 
5.5 km/s v∞ given by launcher | May exceed Ariane 64 capabilites
STATEMENT
Multi Gravity Assist trajectory needed to rendezvous with the comet.
Constraints to perform science at distances from the Sun lower than 3AU.
CRITICALITIES

## Slide 14: Analysis and Trade-offs – MA
184P/Lovas 2
320P/McNaught
304P/Ory
Comet identification:
Jupiter family comets
Condition code = 0 (Uncertainty knowledge)
i < 10°
Perihelion radius (rp): 1.08 < rp < 1.7 [AU]
Flyby sequence analysis:
Tisserand graph e flyby selection
Close Proximity:
Safe approach to the comet
Imaging condition

## Slide 15: Transfer strategy – MA
Transfer to Ory
Departure from Earth: 2033-Dec-29
3 DSMs and 2 Earth gravity assists
Rendevouz with Ory: 2042-Jan-29
∆V = 1.430 km/s
Return to Earth
Departure from Ory: 2042-Dec-04
DSM near the orbit apocenter
Capsule release and Earth divert
∆V = 0.785 km/s
Approach:
PyKep and Pygmo libraries
Multiple runs of the heuristic +slsqp solver
Solution:

## Slide 16: Close Proximity - MA
Approach along track for safety reason
(quasi stable HP)
Sun phase angle span (40° - 90°) for
optimal imaging condition
Initial Target Characterization
Target Mapping
2 Sun Stabilized Terminal Orbits (SSTO) for mapping
2 Altitude levels for safety reasons
Backup: equatorial orbit if spin axis is unfavourable
Total ∆v < 100 m/s
SSTO 1, a = 10 km
SSTO 2, a = 20 km

## Slide 17: Capsule release and divert manoeuvre - MA
Capsule release:
12h before re-entry
Hyperbolic pericentre on Earth surface
Divert manoeuvre:
Right after capsule release
Pericentre raising to 400 km
Earth escape
End of Life (TBD):
Heliocentric graveyard orbit
Mission extension
Terminal guidance

## Slide 18: DV Budget – MA
LAUNCH-COR: Launch correction manoeuvre
DSM: Deep Space Manoeuvre
TCM: Trajectory Correction Manoeuvre
FB: Fly-By
COMET-REND: Comet rendezvous
MANOEUVRE | ∆V [m/s] | Margin | Margined ∆V [m/s]
LAUNCH-COR | 30 | 0 | 30
DSM 1 | 0.01 | 10 m/s | 10.01
TCM-FB 1 | 35 | 0 | 35
DSM 2 | 474.43 | 5% | 498.16
TCM-FB 2 | 35 | 0 | 35
DSM 3 | 788.61 | 5% | 828.04
TCM-REND | 10 | 0 | 10
COMET-REND | 167 | 5% | 175.35
PROX-OPS | 50 | 100% | 100
COMET-DEP | 42 | 5% | 44.1
TCM - EARTH | 35 | 0 | 35
DSM - 4 | 709 | 5% | 744.96
EARTH-DIVERT | 34 | 5% | 35.70
TOT | 2410.54 | - | 2581.32

## Slide 19: AOCS/GNC Francesco Cataffo Marco Cocomazzi Daniele Paternoster

## Slide 20: Requirements and Assumptions – GNC
REQ ID | STATEMENT | COMMENTS
GNC-010 | The dynamics of the comet shall be characterized during approach phase. | 
GNC-020 | Landing Precision wrt to the selected one | From MR or SR, influences
GNC-030 | Landing Velocity | From structure subsystem
GNC-040 | The approach from HP3 to touch-down shall be performed in autonomy. | From TTMTC to ensure the proper utilization of HGA
ASSUMPTIONS
STATEMENT | COMMENTS
Absolute navigation: DDOR ang. accuracy 10nrad | From literature
No drag is considered during the Approach to Landing Phase | Low activity of the comet when this phase occurs
Impulsive manoeuvres | 
CRITICALITIES
STATEMENT | COMMENTS
Sensor sensibility to dust | Low activity of the comet when this phase occurs
Not all hazard detectable from the nominal orbit (SSTO 10 km) | HPs at lower altitude are employed to detect eventual hazard
Autonomous HP3 to Touchdown | Too high telecommunication delays for real-time ops.
Safety, visibility, deploy robotic arm (HP3) | 
Minimize the T&G time | To reduce the battery size
Sensors sensibility to dust  operations.
Not all hazard are detectable from nominal orbit (SSTO at 10km)  HPs at lower altitude.
Autonomous from HP3 to touchdown  too high TC delays for real time ops.
Minimize the T&G time (from EPS)  full thruster usage.
HP: Hold Point

## Slide 21: Navigation – GNC
Baseline design:
Scanning lidar
Wide Angle Camera (60° FOV)  full comet in FOV @h=10km
IMU
DDOR + Range Rate measurement + Range (TBC)
Analysis and trade offs:
Interplanetary navigation – ground based:
  Range measurement: very accurate (≈10m).
  DDOR: angular measurement (≈10nrad accuracy).
  Range rate measurement: very accurate (≈10mm/s).
Relative navigation:
  Optical Camera  navigation around the comet and for navigation for landing up to HP3, support mapping imaging.
  Scanning lidar  navigation for final landing phase (T&G) with dust.
  IMU  robustness.
Relative
Interplanetary
}

## Slide 22
Approach:13.5min Coasting: 3.9min
Impact:5.8s Escape: 5.9min
Constraints:
Vtouch = 0.2 m/s
happroaching= 800 m
Minimize T&G time
FTHmax = 12 N
Vcoast=1 m/s
Full thruster usage
}
}
Touch & Go strategy – GNC

## Slide 23: Requirements and Assumptions – ADCS
REQ ID | STATEMENT | COMMENTS
ADCS-010 | The spacecraft shall not exceed a maximum angular acceleration of 0.17 °/s² | From structural and payload request
ADCS-020 | The subsystem shall be designed to ensure single-failure tolerance | System requirement [SR-01]
ADCS-030 | During remote science mode, the APE shall not exceed 0.1° | From PL requirement, resulting in worst APE for the whole mission
ADCS-040 | During safe mode, the APE shall not exceed 5° | From TTMTC to ensure the proper use of LGA
MAIN REQUIREMENTS
MAIN ASSUMPTIONS
STATEMENT | COMMENTS
No drag is considered during the Approach Phase | Low activity of the comet when this phase occurs
SRP was considered referring to 1 AU | Closest distance to Sun during whole mission
AKE is assumed to be 1/3 of the APE at each mode | Common best practice in mission design
Slew sizing based on a 180° rotation in 20 minutes | From worst case of angle and time across operations

## Slide 24: State Machine and modes – ADCS
SAFE
DETUMBLING
SCIENCE - touch
COMMUNICATION
TRANSFER
SUN POINTING
ORBIT CONTROL
DESATURATION
COMMISSIONING
SCIENCE - remote
GS commanded
GS commanded or Automatic
Automatic
Failure Detection
Notes: In the following slide is presented the state machine for ACDS. There are 9 nominal modes plus the safe one. The transition can be either ground station commanded or automatic, whereas whenever a failure is detected there is the transition to safe mode

## Slide 25: Trade-offs and baseline architecture– ADCS
TRADE-OFFs
RWs are more efficient than CMGs
BASELINE
2 Star Sensors
2 IMUs
8 Sun Sensors
4 RWs
6 Thrusters
Cold redundancy
Retrieve attitude in worst case scenario (no star trackers available)
To have almost full coverage
Pyramidal configuration
Avoid residual torques, most control authority along non vertical axis while landing
Star Tracker integrity: positioning as far away as possible from landing surface
Common thrusters with PS
Notes: In this slide are presented the criticalities met during the desig. During the mission, no high slew rate is required and also considering our mass Reaction wheels are more efficient than CMGs. Another critical point is the configuration of thrusters: the chosen one allows to use common thrusters with propulsion system in order to reduce the number needed. Next inmportant point from requirements is the redundancy. We opted for 2 Star trackers used in cold redundancy in order to have one always available when the other has sun in field of view. Than there are 2 IMUs that in terms of redundancy are needed to allow the retrieving of attitude whenever star sensors are not available. Moving to Reaction wheels, a pyramidal configuration was chosen in order to have always full controllability. Finally we conclude with 6 thrusters to which we add two from PS: the total amount allows to avoid residual torques along each of the three axis

## Slide 26: Propulsion Riccardo Coppola Gabriele Nuccio Angelica Perniciaro

## Slide 27: Requirements and Assumptions – PS
REQ ID | STATEMENT | COMMENTS
PS-01 | The system shall ensure the total ΔV of the mission. | To comply with Mission Analysis.
STATEMENT
Statistics used for Pressure Falls from the Tanks to the combustion chambers.
Thrusters were taken from COTS.
Final Helium pressure equal to tanks pressure.
ASSUMPTIONS
Provide a compact system compatible with mission analysis.
Design a system requiring an affordable power budget.
CRITICALITIES

## Slide 28: Analysis and Trade-offs – PS
3 Alternatives for the main propulsion system:
CP: Bipropellant/Monopropellant
EP: Xe Ion thrusters
CP + EP

## Slide 29: Final Baseline Design – PS
BIPROPELLANT MMH + NTO
15 Ariane Group Bi-propellant thrusters with Dual seat valve
Pressure-fed with Helium
Tanks Material: Ti6Al4V
Tanks Shape: Cylinder + Hemispherical Caps
Pressurant Tank Shape: Spherical
6 thrusters ADCS: Orbit Control, SK, T&G, Slew, De-Tumbling

## Slide 30: Final Baseline Design – PS
BIPROPELLANT MMH + NTO
15 Ariane Group Bi-propellant thrusters with Dual seat valve
Pressure-fed with Helium
Tanks Material: Ti6Al4V
Tanks Shape: Cylinder + Hemispherical Caps
Pressurant Tank Shape: Spherical
5 thrusters PRIMARY PS (SR-01)

## Slide 31: Final Baseline Design – PS
BIPROPELLANT MMH + NTO
15 Ariane Group Bi-propellant thrusters with Dual seat valve
Pressure-fed with Helium
Tanks Material: Ti6Al4V
Tanks Shape: Cylinder + Hemispherical Caps
Pressurant Tank Shape: Spherical
4 thrusters shared ADCS – PRIMARY PS

## Slide 32: Final Baseline Design – PS
Inputs:
ΔV [m/s] = 2581
Choice:
Pc [bar] = 9
Isp [s] = 292
O/F = 1.67
BIPROPELLANT MMH + NTO
15 Ariane Group Bi-propellant thrusters with Dual seat valve
Pressure-fed with Helium
Tanks Material: Ti6Al4V
Tanks Shape: Cylinder + Hemispherical Caps
Pressurant Tank Shape: Spherical

## Slide 33: Results – PS
Feature | Value
Propellant Mass [kg] | 2065.90
Pressurant Mass [kg] | 9.03
Fuel Tank Volume [m3] | 0.973
Oxidizer Tank Volume [m3] | 0.973
Pressurant Tank Volume [m3] | 0.278
Inert Mass of the PS [kg] | 98.45
Outputs:
Overall compact system
Single failure tolerant
Low power budget

## Slide 34: Communication & On Board Data Handling Lorenzo Cesarini Gaetano Vitello

## Slide 35: Communication Strategy – COMMS

## Slide 36: Analysis and Trade-offs – COMMS
Ground network:
ESA Core Network
- LEOP/Commissioning
- Close-to-Earth OPS
NASA DSN
Data Rate vs Distance (HGA):
Phase: Transfer
Distance: 4 [AU]
Data Rate: 10 [kbit/s]
Phase: Science
Distance: 2.6 [AU]
Data Rate: 100 [kbit/s]

## Slide 37
Final Baseline Design – COMMS

## Slide 38: Requirements and Assumptions – OBDH
Main OBC shall be sized to store all Payload data (20 GB)
OBDH shall be sized to withstand total radiation dose absorbed during mission
Main OBC shall be sized for image processing
ID | 
SR-01 | The system shall be single-failure-tolerant
MR-08 | The total mission lifetime shall be at least 8 years
Assumptions
Main OBC Sizing Results
RAM [Mb] | ROM[Mb] | Mass Memory [GB]
2.33 | 4.34 | 20

## Slide 39: Analysis and Trade-offs – OBDH
TID Analysis performed using Spenvis
106 rad absorbed over a 8yr mission at a distance of 1AU
FUSIO RT (Main OBC) tested for 50krad
2mm Al schielding around OBC

## Slide 40: Final Baseline Design – OBDH

## Slide 41: Electrical Power System Cecilia Calegari Giuseppe Brentino

## Slide 42: Requirements and Assumptions – EPS
ID | Requirements
SR-01 | The system shall be single-failure-tolerant
MR-05 | The mission shall be compatible with a European launch vehicle
Assumptions:
The launcher will provide all the electrical power until separation
The solar array will always point toward the sun with an accuracy of 20 degrees.
Negligible eclipse time

## Slide 43: Analysis and Trade-offs – EPS
Power generation:
  Solar array: TJ GaAs by Azurspace, good compromise between cost and efficiency
  RTG: 50% mass savings with respect to PV + batteries, but it is not compatible with Ariane 6
Batteries:
  Li-Ion cells to reduce the mass
  The touch and go maneuver will be performed on battery power, in order to reduce structural loads on the solar arrays
Power distribution:
  Peak Power Tracking with an unregulated bus at 28V in accordance with the literature

## Slide 44: Final Baseline Design – EPS
Batteries | 
Capacity [W-hr] | 8100
Mass [kg] | 70
Nseries | 8
Nparallel | 30
Solar arrays | 
Area [m^2] | 53.4
Mass [kg] | 267
Nseries | 13
Nparallel | 1226
Sizing case:
Phase: Telecom (low power)
Power required: 626 W
Max Sun distance: 4.6 AU
Specific power available: 13 W/m^2
Sizing case:
Survival in Safe mode for 12 hours @4.6 AU

## Slide 45: Power budget

## Slide 46: Thermal Control Luca Frassinella Edoardo Mensi Weingrill Filippo Resta

## Slide 47: Requirements and Assumptions – TCS
System Requirement: SR-03
Hot Case: Earth Flyby
  qSun = 1367 ; qAlbedo = 423.74 ; qIR = 181.12
Cold Case: Max distance from Sun with ME off (~4.9 AU)
  qSun = 202.29
Margins Philosophy Adopted
  Temperature Range = [TMin + 15°C , TMax – 15°C]
  QHeaters / 0.7

## Slide 48: Analysis and Trade-offs – TCS
Subsystem architecture:
Radiators with thermal louvers:
  Surface 3, 5, 6
  Solar arrays
MLI on all external surfaces where free
Heaters on the critical components, mainly on batteries, tanks and P/L
Coatings:
  Black paint for internal surfaces
  White paint for HGA

## Slide 49: Analysis and Trade-offs – TCS
Approach:
Multi-Node Analysis
  20 Nodes
    External surfaces
    External MLI layers
    P/L, TAG arm, batteries, tank, SAs, main engine, radiators
  Assumptions:
    No radiative heat transfer between the panels
    Unique node containing all the tanks, considering the most stringent temperature range
    No transient analysis

## Slide 50: Final Baseline Design – TCS
TEMPERATURE [°C] |  |  |  |  |  | 
 | HOT CASE | COLD CASE | Temperature Ranges [°C] |  |  | 
 | Fly-By at Earth | Comet Approach | Tmin | Tmin.MM* | Tmax | Tmax.MM*
SA1 | 51.8 | -117.4 | -150 | -135 | 150 | 135
SA2 | 51.8 | -117.4 | -150 | -135 | 150 | 135
TAG | 63.1 | -92.9 | -125 | -85 | 100 | 85
PL | 3.2 | -52.7 | -50 | -35 | 50 | 35
BATT | 30.9 | 13.8 | 0 | 15 | 35 | 20
TANK | 22.5 | 2.3 | 0 | 15 | 40 | 25
Final Architecture | 
Radiators Surface with Louvers (Arrays excluded) [m2] | 11.9
N.of Heaters | 20
* Margined according to the margin philosophy

## Slide 51: Final Baseline Design – TCS

## Slide 52: Configuration Giacomo Burlando Tommaso Cesarini

## Slide 53: Configuration
INTERNAL and EXTERNAL configuration
HGA
Body | 2.3 x 2.3 x 2.1 m
Single solar array | 9.45 x 2.55 m
Adapter
Thrusters
Robotic arm
Tanks
Sample return capsule
Radar
LGA
Boom with magnetometer

## Slide 54: Configuration
Fairing envelope Ariane 64 with DORY
Stowed conf. | 3.82 x 3.05 x 2.92 m
Fairing (Ø, H) | 5.4 x 20 m

## Slide 55: Structure Riccardo Galvani Mattia Sala Riccardo Caliri

## Slide 56: Structure - R.A.D.
Costraints |  | Output
Sampling time |  | 
Maximum acceleration |  | 
Momentum balance |  | 
Maximum displacement |  | 
Costraints |  | Output
Sampling time |  | 
Maximum acceleration |  | 
Momentum balance |  | 
Maximum displacement |  | 
Notes: In this phase of the study, we defined the design constraints for the robotic arm during a touch-and-go maneuver. These constraints directly influence the selection of key parameters, summarized as follows:
Sampling time: To ensure the minimum mass of sample required in the mission objective a minimum sampling time of 5 seconds was stated based on the experiment performed during the osirix rex mission preparation.
Maximum acceleration: The spacecraft’s structural limits, particularly the flexibility of the solar panels, led us to set a maximum allowable acceleration of 0.04 m/s².
Momentum balance: To account for potential offsets in the center of mass and resulting torques, we used a moment equilibrium equation involving the spring and thrusters. From this balance, we derived the required spring stiffness that keeps the attitude disturbance within the correction capacity of the 10 N thrusters.
Maximum displacement: The arm’s spring displacement was limited to 0.5 meters. This constraint, related to the overall size of the mechanism, ensures that the energy stored and released remains within controlled bounds.
Each constraint leads to a corresponding design output: sampling time, maximum arm-induced acceleration, spring stiffness, and maximum displacement. Together, they define a robotic system that is stable, structurally compatible, and capable of performing precise touch-and-go operations in space

## Slide 57: Structure: TAGSAM & Robotic Arm
Description | Data
Base diameter | 0.23 m
Height | 0.053 m
Material selected | Al 7075
Dry mass to store in return capsule | 0.91 kg
Allowable sample volume | 0.374 L
Arm full extention | 3.4 m
Arm diameter | 0.006 m (TBC)
SHOULDER
ELBOW
WRIST
N2 BOTTLES
COLLECTION HEAD
SHOULDER
COLLECTION RESERVOIR
HOLES FOR N2 FLOW
DETACHABLE COMPONENT
38 μm OPENINGS
Extensive IRAD-supported LM testing
Test results fulfil collection requirements
Shoulder and Elbow EMs to size
Wrist U-joint to adapt to the ground
(Heritage: OSIRIS-REx)

## Slide 58: Structure: Modal Analysis
Launcher compliance | Value
Min. axial natural frequency | 20 Hz
Min. lateral natural frequency | 6 Hz
Min. ax. obtained | 29 Hz
Min. lat. obtaned | 13 Hz
Zone | Selected materials
Skin e core | Aluminum and honeycomb composite layup.

## Slide 59: Mass budget
Subsystem | Mass with DMMs[kg]
P/L | 43.03
ADCS | 50.72
GNC | 33.47
EPS | 413.88
TTMTC | 68.88
TCS | 11.34
PS | 98.45
OBDH | 1.20
CAPSULE | 27.3
STRUCTURES | 420
Dry Mass (+20%) | 1497.91
Wet Mass | 3563.81
Launch Mass | 3643.81
- Design Maturity Margins
for subsystems are applied in compliance with ECSS standards.
- Mass currently not compliant with Ariane 64 C3 capabilities, but addressable in further iterations.

## Slide 60: Cost Gaetano Vitello

## Slide 61: Final Baseline Design – COST
System activities cost:
Management
Engineering
Product assurance
AIVT
Planetary Protection
Facility
Chart: 
| AOCS | PROP | EPS | COMM | OBDH | STR | TCS | PL | OPERATIONS | LAUNCH | SYSTEM ACTIVITIES
Cost Breakdown | 8.7 | 4.2 | 40 | 13 | 19 | 12.1 | 2.25 | 123 | 96 | 120 | 170
Total no margin: | 636.93 M€
Total + 31% risk margin: | 834.43 M€
Operation:
DSN Ground Station
MOC, SOC
Payload Instrumentation.

## Slide 62: Mission Requirements Overview

## Slide 63: System Requirements Overview

## Slide 64: Conclusions
The mission is deemed feasible, and can go through further studies to address open points and criticalities
Open points
Ariane 64 currently insufficient
Further design iteration needed on all subsystems
If an European launcher is not selected, RTGs can be evaluated as power source alternative
Re-iterate mission design with Electric Propulsion
Samples management (Pressure, Temperature)

## Slide 66: Open Points – Payload
Mass Spectrometer
Neutron Detector
Camera imaging optimization

## Slide 67: Backup Slide – Mission Analysis

## Slide 68
EPS: Power budget

## Slide 69: Structure: Backup_slide_RA_aS.
Robotic Arm Control |  | u.o.m
Inertia of the arm |  | 
Time and velocity |  | -
Torque needed |  | 
Robotic Arm Control |  | u.o.m
Inertia of the arm |  | 
Time and velocity |  | -
Torque needed |  | 
Max Acceleration During Slew |  | u.o.m
Panel stiffness |  | 
Maximum displ |  | 
Maximum acc. |  | 
Max Acceleration During Slew |  | u.o.m
Panel stiffness |  | 
Maximum displ |  | 
Maximum acc. |  | 

## Slide 70: Structure: Modal Analysis